## Slide 1: ENGI 301 Plant Water Reminder Proposal
October 4, 2020
Fernanda Lago Arroyo

## Slide 2: Background Information
What is being proposed?
  A system that texts plant owner to remind them to water their plants and notifies them if their plants are not receiving the correct amount of sunlight
What improvements will be on existing projects?
  Will send text notifications rather than email notifications
    Notifications based off plants receiving appropriate water and sunlight
    Suggests whether to expose or shield plant to sunlight
  Will include light sensor in addition to soil humidity sensor
  Will build enclosure for device
https://www.digikey.com/en/articles/how-to-make-a-beaglebone-based-appliance-notification-texter
https://www.hackster.io/MatinaStef/to-water-or-not-to-water-7204fe

## Slide 3: UX Design
Steps for user interacting with device:
  1. Wall plug in. Turns on device using switch, light flickers on next to switch.
  2. Display outputs a message detailing how the soil humidity and light levels of the plant
  3. If these are inadequate, user will receive a text.
Set up needs:
    User must load phone number beforehand on laptop
    User must connect device to Wi-Fi
    Text message is sent twice a day if levels are inadequate

## Slide 4: System Block Diagram
Pocket Beagle
USB and
WI-FI Dongle
TL-WN725N
miniUSB
I2C Soil Sensor
4026
Light Sensor
TEMT6000
49 I2C2SCL
51 I2C2SDA
63 VDD3V3
61 GND
18 VDD3V3
20 GND
23 AIN0
TFT LCD Touchscreen
ILI9341
SPICLK
MISO
MOSI
CS
D/C

## Slide 5: Power Block Diagram
Pocket Beagle
Vin: USB or Cell Battery
Vout: 1.8 V (analog), 3.3 V, and SYS (switched Vin)
I = 500 mA
USB and
WI-FI Plug-in
Vin: 5V
I = 500 mA
I2C Soil Sensor
Vin: 3-5 V
I = 80 mA
Light Sensor
Vout: (Analog voltage to signal pin): <6V
I = 20 mA
miniUSB
Vout: 5V
TFT LCD Touchscreen
ILI9341
Vin: 3.3 V
I = 100mA

## Slide 6: Components / Budget
Component | Need to Buy | Cost
Adafruit STEMMA Soil Sensor - I2C Capacitive Moisture Sensor | Yes | $7.50
TP-LINK TL-WN725N Network adapter USB 2.0 802.11n, 802.11g, 802.11b | Yes | $10.99
SparkFun Ambient Light Sensor Breakout - TEMT6000 | Yes | $4.25
TFT LCD Touchscreen ILI9341 | Yes | $ 5.99