## Slide 1: ENGI 301 Plant Reminder Box: PCB Proposal
11/20/20
Fernanda Lago

## Slide 2: Functionality
PCB consists of:
    PocketBeagle
        Main hardware computer for running the scripts and gathering data
    USB adapter for wifi dongle
        To connect the device to the wifi
    Light sensors
        To sense level of light plant is receiving through average value
    Soil Humidity sensor
        To sense whether plant has received enough water
    LCD Screen
        To display the light and water status of the plant
Summary: PCB houses all components necessary to the function of the Plant Reminder Box

## Slide 3: High-Level Functional Block Diagram
USB Female Breakout
(for wifi dongle)
LCD Screen
PocketBeagle
USB1
SPI0
Light Sensors
AIN0 and AIN1
GPIO
Soil Sensor
I2C0

## Slide 4: Power Block Diagram
USB Female Breakout
(for wifi dongle)
LCD Screen
PocketBeagle
3.3 V
3.3 V
Light Sensors
<6 V
Soil Sensor
3-5 V

## Slide 5: Mechanical Block Diagram
LCD Screen (2.38” x 1.68”)
3”
0.31”
2”
PocketBeagle
(2.21” x 1.38”)
Light Sensor
(0.55” x 0.25”)
Light Sensor
(0.55” x 0.25”)
TOP
BOTTOM
1”
0.55”
LED
USB Connector
(2.21” x 1.38”)
Soil Sensor
Microcontroller